## Slide 1: Waveform Optimisation for Information and Power Transfer
The Nonlinear Harvester Model and Rate-Energy Tradeoff
Yang Zhao (yang.zhao18@imperial.ac.uk)
Waveform Optimisation for Information and Power Transfer
15 Feb. 19

## Slide 2: Wireless Information and Power Transfer (WIPT)
Energy harvest models (linear, nonlinear)
Rate-energy (R-E) region characterisation
Transmitter and receiver architecture
Waveform design
Modulation
Beamforming and input distribution
Resource allocation
RF spectrum use
Waveform Optimisation for Information and Power Transfer
15 Feb. 19
“A WIPT system should therefore be designed such that the RF radiation and the RF spectrum are exploited in the most efﬁcient manner to deliver both information and energy.”
Topics
B. Clerckx et al, "Fundamentals of Wireless Information and Power Transfer: From RF Energy Harvester Models to Signal and System Designs," in IEEE Journal on Selected Areas in Communications, vol. 37, no. 1, pp. 4-33, Jan. 2019.
Image by IoT connection. Adapted from IoT Services and Solutions provider for Business, by Credencys Solutions Inc., 2019, retrieved from https://www.credencys.com/iot-solutions/. Copyright by Credencys Solutions Inc.

## Slide 3: Waveform Optimisation
To enlarge the R-E region
To improve spectrum and power efficiency
To support numerous low-power devices
To boost the revolution in IoT
Why?
Channel (adaptive signal based on CSIT to enhance rate)
Receiver (suitable waveform favoured by rectenna to maximise energy)
Where?
Waveform Optimisation for Information and Power Transfer
15 Feb. 19
Identify the fundamental tradeoff between information and power transfer
Evaluate linear and nonlinear harvest models
Investigate beamforming, power allocation, waveform, modulation, and input distribution
What?
Formulate the optimisation problem as an energy maximisation problem
Superpose a deterministic power waveform to a communication waveform
Twofold benefit: energy (multisine > modulated), rate (deterministic, no interference)
How?

## Slide 4: SWIPT Diagram
Waveform Optimisation for Information and Power Transfer
15 Feb. 19
Simultaneous WIPT
Blocks of WIPT system
Problem: to maximise the overall power efficiency
: efficiency of the transmit antenna -> efficient power amplifier
: efficiency of the channel -> adaptive signals
: efficiency of the rectenna -> rectenna and input signal design
Diode linear model: and are independent of input signal power and shape (optimise , , separately)
Diode nonlinear model: , , are coupled, is a nonlinear function of the input signal (jointly optimise )
B. Clerckx et al, "Fundamentals of Wireless Information and Power Transfer: From RF Energy Harvester Models to Signal and System Designs," in IEEE Journal on Selected Areas in Communications, vol. 37, no. 1, pp. 4-33, Jan. 2019.

## Slide 5: Diode Nonlinearity and Harvester Models
Waveform Optimisation for Information and Power Transfer
15 Feb. 19
Diode characteristics
R1: region of diode linear model
R2: region of diode nonlinear model
Boundary ():
-20 dBm for continuous wave
-30 dBm for multisine
Diode current and DC current:
Diode DC current (determines output power):
Diode linear model:
Input power is proportional to the output power
Independent of the power and shape of the received signal (averaged out)
Holds for very low where high order terms are negligible [Region 1]
Diode nonlinear model:
Truncating at higher order leads to nonlinear behaviour ( related to waveform)
Holds when the high order terms are not negligible [Region 2]
Suitable for multisine input waveform
B. Clerckx et al, "Fundamentals of Wireless Information and Power Transfer: From RF Energy Harvester Models to Signal and System Designs," in IEEE Journal on Selected Areas in Communications, vol. 37, no. 1, pp. 4-33, Jan. 2019.

## Slide 6: Multisine and Efficiency
Waveform Optimisation for Information and Power Transfer
15 Feb. 19
B. Clerckx, “Wireless Information and Power Transfer: Nonlinearity, Waveform Design and Rate-Energy Tradeoff,” IEEE Trans. on Sig. Proc., vol 66, no 4, pp 847-862, Feb. 2018.
Harvested DC power vs average input power and RF-to-DC conversion efﬁciency
Multisine waveform used as a voltage source and the rectiﬁed output voltage
Multisine waveform:
High peak-to-average power ratio (PAPR)
Concentrated power triggers the diode
Pulse amplitude determined by number of tones N
The larger the number of tones N, the larger is the magnitude of the pulses and therefore the larger is the output voltage at the time of discharge.

## Slide 7: Receiver Architectures
Waveform Optimisation for Information and Power Transfer
15 Feb. 19
Ideal, TS and PS receivers
EH:
energy harvester
ID:
information decoder
Ideal receiver: use the same signal for both ID and EH receivers
Optimal but not realisable
Time switching (TS) receiver: switch the signal to either ID or EH receiver
Transmission block -> power block / data block (orthogonal)
Optimise waveforms for individual blocks
R-E tradeoff depends on slot length and the transmit signals
Power splitting (PS) receiver: split a portion of the signal to ID receiver and the rest to EH receiver
Received signal -> power signal () / data signal ()
Optimise the transmitted signals jointly
R-E region depends on PS ratio and the transmit signals
B. Clerckx et al, "Fundamentals of Wireless Information and Power Transfer: From RF Energy Harvester Models to Signal and System Designs," in IEEE Journal on Selected Areas in Communications, vol. 37, no. 1, pp. 4-33, Jan. 2019.

## Slide 8: Problem Formulation
Waveform Optimisation for Information and Power Transfer
15 Feb. 19
B. Clerckx, “Wireless Information and Power Transfer: Nonlinearity, Waveform Design and Rate-Energy Tradeoff,” IEEE Trans. on Sig. Proc., vol 66, no 4, pp 847-862, Feb. 2018.
The R-E region is defined as:
The optimisation problem turns into an energy maximisation problem:
… and can be transformed to Geometric Program then solved by the algorithms proposed by the paper
Rate does not exceed mutual information
Output current is no larger than diode DC current
Resource spent on energy and information components no more than budget

## Slide 9: Algorithm: Single-Input
Waveform Optimisation for Information and Power Transfer
15 Feb. 19
B. Clerckx, “Wireless Information and Power Transfer: Nonlinearity, Waveform Design and Rate-Energy Tradeoff,” IEEE Trans. on Sig. Proc., vol 66, no 4, pp 847-862, Feb. 2018.
is the monomial terms in the posynomial
is the monomials of the posynomial

## Slide 10: Algorithm: Multiple-Input
Waveform Optimisation for Information and Power Transfer
15 Feb. 19
B. Clerckx, “Wireless Information and Power Transfer: Nonlinearity, Waveform Design and Rate-Energy Tradeoff,” IEEE Trans. on Sig. Proc., vol 66, no 4, pp 847-862, Feb. 2018.
Spatial and frequency domain decoupling
MRT beamformers by (42) convert the problem into single-antenna case
Reduced complexity ()

## Slide 11: Algorithm: Lower-Bound
Waveform Optimisation for Information and Power Transfer
15 Feb. 19
B. Clerckx, “Wireless Information and Power Transfer: Nonlinearity, Waveform Design and Rate-Energy Tradeoff,” IEEE Trans. on Sig. Proc., vol 66, no 4, pp 847-862, Feb. 2018.
Forcing : the power waveform is CSCG rather than deterministic multisine
Twofold benefit disappears; interference with power and therefore rate loss

## Slide 12: Result: Power Waveform
Waveform Optimisation for Information and Power Transfer
15 Feb. 19
B. Clerckx, “Wireless Information and Power Transfer: Nonlinearity, Waveform Design and Rate-Energy Tradeoff,” IEEE Trans. on Sig. Proc., vol 66, no 4, pp 847-862, Feb. 2018.
R-E region as a function of for MHz and dB

## Slide 13
Waveform Optimisation for Information and Power Transfer
15 Feb. 19
B. Clerckx, “Wireless Information and Power Transfer: Nonlinearity, Waveform Design and Rate-Energy Tradeoff,” IEEE Trans. on Sig. Proc., vol 66, no 4, pp 847-862, Feb. 2018.
R-E region for MHz and dB

## Slide 14: Analysis and Conclusions
Waveform Optimisation for Information and Power Transfer
15 Feb. 19
With superposed waveforms, increasing N boosts the harvested energy
The multisine power waveform is always useful in nonlinear model
Gain over lower-bound increases as the SNR increases
A combination of power splitting and time sharing is the best strategy
At low SNRs (10, 20 dB), PS < TS; at high SNRs (30, 40 dB), PS > TS
PS is favoured for low N, combination for medium N and TS for large N
Multisine + modulated waveform with CSCG = non-zero mean Gaussian
Threshold R ↓ power allocated to the multisine waveform ↑

## Slide 15: Thank you!
Waveform Optimisation for Information and Power Transfer
15 Feb. 19